## Slide 1: VHF/UHF Wireless Uplink Solutions for Remote Wireless Sensor Networks
KTH Royal Institute of Technology
Alp Sayin
22 May 2013
sayin[at]kth[dot]se

## Slide 2: outline
Background
Problem
Goals
Theory
Design
Implementation
Experiments
Results
Conclusions
Future Work
Q & A

## Slide 3: background - general
Atmel ATMega128RF-chip with IEEE 802.15.4Transceiver as Mote
The mote software is based on the Contiki operating system.
A mote automatically becomes a sink mote when connected via a TTL/USB converter
Gateway is usually a Bifrost/Alix system or Raspberry Pi without internet connection

## Slide 4: background - sensors
Sensors
  Pressure
  Temperature
  Precipitation
  Soil moisture
  Solar efficiency
  Drinking water quality
    Turbidity
    Acidity
    Redox-potential

## Slide 5: background - motes
MCU
  Atmel ATMega128Rfa1
    Internal ADC
    Built-in IEEE 802.15.4 Radio Transceiver
OS
  TinyOS
    NesC
  Contiki-Os
    C99

## Slide 6: background - communication
Inter-node communication
  IEEE 802.15.4
    10-20 meters range
    250 kbit/s raw data rate
  Contiki Rime Protocol
Sink-Gateway communication
  RS232 Uart Communication
  Sensd by Robert Olsson and Jens Laas

## Slide 7: background - gateway
Sink Node
  Any Herjulf mote can be used as a sink node
    No extra programming required
Gateway
  Alix 2d13 machine
    Bifrost Os
    Voyage Linux

## Slide 8: background - uplink
Uplink
  Cabled connection
    Fiber optic
    Ethernet cables
  Wireless connection
    GSM network (GPRS, HSDPA etc.)
    Satellite link
    Dedicated terrestrial wireless link on a suitable frequency
  Physical transportation of data
    Delay tolerant network

## Slide 9: problem
Get the collected data out from the gateway of a WSN to a remote repository with internet access.
Explore 434 MHz and 144 MHz frequencies and associated protocol stacks to optimize the range and QoS
Try from dedicated hardware solutions to software defined radio links to optimize power consumption and flexibility.

## Slide 10: goals
A feasible, minimum hardware, low-cost, low-power, long range solution to the problem of getting the sensor data out from the sink mote to a remote repository
To implement IP over the same solution, so that existing user programs, or newly developed programs could be used over this link

## Slide 11: theory – physical link
VHF / UHF Bands
  144 Mhz Band (2 m band)
  433 Mhz Band (70 cm band)
Modulation
  Bi-phase encoding (Manchester)
  1200 baud AFSK

## Slide 12: theory – data link
ONLY FRAME FORMAT!
  Ethernet
    Max payload 1500 byte
    18 bytes header
      6 byte source and destination
      2 byte length
      4 byte CRC checksum
  IEEE 802.15.4
    Max payload 256 byte
    21 bytes header
      2 byte frame control
      1 byte sequence number
      4-20 byte address information
      2 byte frame check sequence
  AX.25
    Max Payload 256 byte
    18 bytes header
      7 byte source and destination
      1 byte control
      1 byte protocol identifier
      2 byte CRC checksum

## Slide 13: theory – network layer
IP
  IPv4
    20 byte header
      4 byte source and destination
      2 byte header checksum
      2 byte total length
      1 byte time-to-live
  IPv6
    40 byte header
      16 byte source and destination
      2 byte payload length
      1 byte time-to-live
APRS
  Rests on AX.25
  Text based protocol
  No header requirement except AX.25 headers

## Slide 14: theory – transport layer
UDP
  Easy to implement, difficult to use
TCP
  Difficult to implement, easier to use
APRS
  Pseudo-routing routines are implemented
  Based on broadcast flooding with reverse poisoning

## Slide 15: theory – application layer
HTTP
  Simple request/response protocol
  Can be used for any resource access application
  Requires TCP
TFTP
  An old yet reliable protocol (still used in some routers for flashing)
  Can work on UDP
  Has limitations (e.g. file size < 4 GB)
APRS
  Generally used for weather and location reporting
  Also has a telemetry message option for reporting arbitrary measurements
  Messages are collected in a single open repository (accessible via aprs.fi)

## Slide 16: theory - hardware
TNC with Radio rigs
  Radio
    MAAS AHT-UV-2
    YAESU FT8900
  TNC
    Hardware TNC
    Software TNC
      soundmodem
Dedicated Radio modules
  Radiometrix Bim2A
  Radiometric UHX1

## Slide 17: design - protocols
AX.25
IPv4
TCP
UDP
APRS
APRS
Data-Link
Network
Transport
Application
HTTP
TFTP
APRS
Physical
VHF/UHF Analog or Digital Modulation
Figure.1 Resulting branches in the project after design decisions

## Slide 18: design - final
HTTP/TCP/IPv4/AX.25
Soundmodem
Analogue Modulation
Linux Platform
TFTP/UDP/IPv4/AX.25
Radiotftp
Digital Modulation
Linux Platform
Radiotunnel
Digital Modulation
Linux Platform
Radiotftp_process
Digital Modulation
Contiki Platform
APRS/AX.25
APRS
Analogue Modulation
Linux Platform
Figure.2 Resulting solutions after hardware decisions

## Slide 19: implementation - radiotftp
TFTP < UDP < IPv4 < AX.25 < Bi-phase Encoded Digital Stream
Tailored solution for the problem
Completely in C, easier to port
Figure.3 System diagram for radiotftp solution

## Slide 20: implementation – radiotftp_process
TFTP < UDP < IPv4 < AX.25 < Bi-phase Encoded Digital Stream
Tailored solution for the problem
Contiki-Os over Atmega128Rfa1 port of radiotftp
Figure.4 System diagram for radiotftp_process solution

## Slide 21: implementation - radiotunnel
IPv4 > AX.25 > Bi-phase Encoded Digital Stream
Flexible solution, open for any application layer compatible with UDP or TCP
Easy to implement with use of virtual kernel interfaces
Figure.5 System diagram for radio_tunnel solution

## Slide 22: implementation - soundmodem
IPv4 > AX.25 > AFSK Analog Stream
Flexible solution, open for any application layer compatible with UDP or TCP
Software is already there
Requires more hardware
Figure.6 System diagram for soundmodem solution

## Slide 23: implementation - aprs
APRS > AX.25
Utilizes the APRS network
Limited by APRS and radio amateur rules
Figure.7 System diagram for APRS solution

## Slide 24: experiments
Radiotftp
  Parameters: Distance, Transfer Size
  Outputs: Transfer Time, Packet Error Rate, Power Consumption
Radiotunnel
  Parameters: Transfer Size
  Outputs: Transfer Time, Channel Utilization, Power Consumption
Soundmodem
  Parameters: Transfer Size
  Outputs: Transfer Time, Channel Utilization, Power Consumption
General Experiments with Radiometrix Devices
  Parameters: Distance
  Outputs: Received Signal Strength Indicator (RSSI)

## Slide 25: experiments – outdoor map
2120 meters
1950 meters
1820 meters
1390 meters
1050 meters
700 meters
395 meters
Figure.8 Map of Gamla Stan Experiments (image from Google Maps)

## Slide 26: results
 | Transfer Time 127 bytes | Transfer Time 2 kbytes
radiotftp uhx1 | 00:08.915 | 00:21.727
radiotftp bim2a | 00:00.873 | 00:02.414
radiotunnel uhx1 | 02:56.029 | 12:09.429
radiotunnel bim2a | 02:00.120 | 02:05.261
soundmodem | 02:09.707 | 02:59.324
Table.1 Average transfer times with minimum distance between transceivers

## Slide 27: results – transfer times
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Transfer Time for 144 Mhz with 127 bytes (sec) | 2.4141 | 2.4172 | 5.8604 | 6.6321 | 3.6759 | 0 | 3.1727 | 4.1403
Transfer Time for 433 Mhz with 127 bytes (sec) | 0.8727 | 6.6522 | 0 | 0 | 11.5138 | 0 | 0 | 0
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Transfer Time for 144 Mhz with 2 kbytes (sec) | 21.7267 | 21.7249 | 22.635 | 22.7599 | 23.1693 | 0 | 22.1851 | 23.5792
Transfer Time for 433 Mhz with 2 kbytes (sec) | 8.9151 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Figure.9 Transfer time plots for single packet delivery
Figure.10 Transfer time plots for many-packet delivery

## Slide 28: results – packet error rate
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Error Rate for 144 Mhz with 127 bytes (percent) | 0 | 0 | 20.37 | 15.57 | 11.11 | 100 | 6.67 | 14.44
Error Rate for 433 Mhz with 127 bytes (percent) | 0 | 33.46 | 100 | 100 | 71.43 | 100 | 100 | 100
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Error Rate for 144 Mhz with 2 kbytes (percent) | 0 | 0 | 1.96 | 1.68 | 1.13 | 100 | 0.65 | 3.44
Error Rate for 433 Mhz with 2 kbytes (percent) | 3.26 | 100 | 100 | 100 | 100 | 100 | 100 | 100
Figure.11 Error rate plots for single packet delivery
Figure.12 Error rate plots for many-packet delivery

## Slide 29: results - bitrate
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Bitrate for 144 Mhz with 127 bytes (bytes/sec) | 52.6076 | 52.5401 | 21.6709 | 19.1493 | 34.5494 | 0 | 40.029 | 30.6741
Bitrate for 433 Mhz with 127 bytes (bytes/sec) | 145.5254 | 19.0914 | 0 | 0 | 11.0302 | 0 | 0 | 0
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Bitrate for 144 Mhz with 2 kbytes (bytes/sec) | 94.2619 | 94.2697 | 90.4793 | 89.9828 | 88.3928 | 0 | 92.3142 | 86.8562
Bitrate for 433 Mhz with 2 kbytes (bytes/sec) | 229.7226 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Figure.13 Bitrate plots for single packet delivery
Figure.14 Bitrate plots for many-packet delivery

## Slide 30: results – RSSI
Location | RSSI (UHX1) | RSSI (Bim2a)
No Signal Applied | 64 | 0.28
0 (Base) | 196 | 0.48
1 | 136 | 0.40
2 | 122 | 0.30
3 | 116 | 0.31
4 | 133 | 0.38
5 | 103 | N/A
6 | 126 | N/A
7 | 121 | N/A
Table.2 RSSI readings from various locations with UHX1 and Bim2A

## Slide 31: conclusions - radiotftp
The effect of overhead can be heavily observed. On the other hand, many-packet transactions are statistically more probable to disconnect (‘Experiments with radiotftp’).
The bitrate difference in bands shows itself also in the final throughput.
While using the 2 meter band, the distance does not seem to have much effect. On the other hand, obstructions on the wave path cause a lot of distortion.
While using the 70 cm band, the received power decays much more relative to the 2 meter band and therefore observed to have a much shorter range.
In both bands having a high ground has a good impact on signal strength.

## Slide 32: Conclusions - general
Radiotftp solution seems to have much greater bitrate compared to others, but this is simply an effect of utilizing the channel more efficiently. On the other hand, other solutions can’t use the channel this efficiently, even if they wanted to.
The radiotunnel solution shows almost an exponential growth in transfer time with respect to the file size. This is due to the manual forced drop of the packets to ensure half-duplex operation.
Soundmodem proved itself to be a faster option compared to radiotunnel, even with its low raw bitrate (1200 bps).
If the radiotunnel is not to be improved to act as an half-duplex interface, and if soundmodem solution can be improved to use radiometrix devices, then radiotunnel solution can deprecated.
Some suggestions could be made according to some requirements:
  If higher throughput is required; radiotftp,
  If easy-setup and easy API is required; radiotunnel
  If standardization and easy API is required; soundmodem
  If standardization and set-it-and-forget-it kind of application is required; APRS solution would be suggested.

## Slide 33: future work - radiotftp
The radiotftp code base should be improved to have multiple-size queues and multiple timers. It already supports it, but it is not a default.
The radiotftp code should be cleaner for further developers. It should look like an open API -which, it is-, and there should be an open documentation for it.
The radiotftp solution can be optimized more by changing the place of the delays and/or replacing the delays with non-busy waits.

## Slide 34: future work – radiotftp_process
The radiotftp_process code could be optimized to work with higher baudrates than 2400. So that it would consume less CPU time while transmission.

## Slide 35: future work - radiotunnel
The radiotunnel code should not be improved anymore, but instead, an actual device driver should be written for fine tuning.

## Slide 36: future work - soundmodem
The soundmodem solution should be moved on to work with Radiometrix devices. In such way, a more portable hardware can be obtained. And the users won’t need to worry about handheld radios’ power consumption.

## Slide 37: future work - APRS
If possible, the APRS solution should also be tested in open field and packet loss should be recorded.

## Slide 38: future work - general
The uhx1_programmer can be extended to be able to program the frequency of the UHX1 devices, so that frequency can be selected while running to avoid interference.
The devtag library could be incorporated to use USB device tags instead of USB device names to select the proper USB FTDI device.
A team has already started working on an implementation of a Delay Tolerant Network (DTN) based on this project’s outcomes.

## Slide 39: questions & answers
Thank you for listening
More information:
  http://alpsayin.com/vhf_uhf_uplink_solutions_for_remote_wireless_sensor_networks
  http://github.com/alpsayin
  http://code.google.com/p/kth-wsn-longrange-radio-uplink/ (old)
  sayin[at]kth[dot]se
WSN Team 2012
  http://ttaportal.org/menu/projects/wsn/fall-2012/
  https://github.com/organizations/WSN-2012
  https://docs.google.com/presentation/pub?id=1rL40Es9D6ZoAD4bN72XcnrYqhL56eWsP8E4WOMR8C-E&start=false&loop=false&delayms=3000

## Slide 40: extra - future work
Figure.15 Topology of a VHF Link with a Delay Tolerant Network as fallback
*Courtesy of WSN Team 2012 (KTH Communications System Design, Design Project Team)

## Slide 41: extra - delay tolerant network
Spectrum Database Radio(SDB) Solution
Selection Mechanism Implementation
Figure.16 Topology of VHF link part of the WSN Team’s project
*Courtesy of WSN Team 2012 (KTH Communications System Design, Fall 2012 Design Project Team)

## Slide 42: extra - demo
Wireless Sensor Network
This Computer
UHF Uplink with RadioTftp
RaspberryPi Gateway
Sink Mote
Figure.17 Topology of the demo setup